Flow scheduling for Multiparty live streaming

---
Multiparty live Streaming: Overview
Alice
Bob
Carol
Dave
Server
Bob
Carol
Dave
Alice

---
Motivations
In current multi-flow streaming, streams are transparent to each other. For the best occasions, each streams large I frame comes like round-robin, in the example below makes the transport time about 100-150ms.
But in the worst occasions, all I frames comes together, make the transport time about 400ms.
Large transport time leads to low flexibility. Here we define flexibility as remain playback time when disconnected, the same as the buffered video time on the client side. The delay is consist of flexibility time and transmission time. We consider delay with larger flexibility time more healthy.

---
Motivations
To meet the demand of high QoE, the video quality we transmit is as high as possible, which lead to low healthy time under given delay limit.
When B and E layer are coupled, client should wait until 400ms to get the first frame, when we set the delay as 400ms, the flexibility time is 0,
compared to Base layer only with 120ms transmission time and 280 flexibility time.
When the layers are decoupled, as shown right, the base video can be watched in after 120ms, and the enhanced layer is finished almost at the same time compared to the coupled one, leads to the result that we get 280ms extra low quality flexibility time. In this occasion, we can watch 280ms low quality video even the client is disconnected, compared to immediate stall in coupled ones.

---
Scheduler
P frame
I frame
Carol’s Scheduler in the server
B Layer
Alice’s Queue
Incoming frames from Alice, Bob and Davis
E Layer
Outgoing frames
S
B Layer
Bob’s Queue
E Layer
B Layer
Dave’s Queue
E Layer
Decision

---
Challenges
Design the Scheduler
Implement a simulator